Late Model and Limited Late Model Safety Check List

___	Good floor boards and firewalls with no holes

___ 	Windshield screen or bars

___	No fluid reservoirs, radiators, batteries, etc. in drivers compartment

___	Battery safely mounted

___	Easy access to the driver from either side

___	No raised edges inside of car

___	Square frames must be 2” x 2” minimum, round tube frames must be min. 1 ¾”.  Minumum  wall thickness is .083”

___	4 post roll cage with gussets and welded to frame

___  	Min. 3 - 1 ½” diameter bars in the drivers door

___	Roll bar padding around driver

___	5 part quick release safety belts no older than 3 years

___	Seat belts properly mounted to the frame of the car

___	Good racing drivers seat mounted firmly to frame

___	If stock transmission and clutch, must have blow proof bellhousing

___	Drive shaft hoop must be installed near the front u-joint

___	Driveshaft & weights painted white or silver with car # on them

___	All weights securely fastened with a minimum of  2 ,  ½” diameter  or larger bolts

___	Front tow hook installed

___	Fuel cell completely visible from rear of car, mounted no lower than rearend

___ 	Fuel cell mounted securely in trunk area inside 20 guage metal box supported by 2

1/8 x 2 steel straps

___	No plastic brake lines

___	Mufflers installed

___	Full face racing helmet, Snell 90 or newer

___	Approved fire resistant uniform and gloves with  SFI rating and no holes no older than 5 years